## Slide 1: US Powerboating Safe Powerboat Handling / Safety and Rescue Boat Handling Day One

## Slide 2: Hull Types and Characteristics
Flat Hulls [planing] SPR p.4
  Easily get on a plane at high speeds
  Designed for calm, flat water
  Not very stable
  Excessive slide when maneuvering

## Slide 3: Hull Types and Characteristics
Deep V [planing] SPR p.5
  Similar to flat bottom but designed to cut through water
  Good steering ability at high speeds
  Perform well in waves in speed; tend to roll at rest

## Slide 4: Hull Types and Characteristics
Cathedral Hull [planing] SPR p.5
  Two or three v-shapes forward, flat in back
  Good stability at rest and at speed
  Rough at speed in waves
  Usually have a lower freeboard

## Slide 5: Hull Types and Characteristics
Soft-Inflatable Hulls [planing] SPR p.5
  Poor driving ability (excessive slide)
  High stability
  High load capacity
  Very wet ride

## Slide 6: Hull Types and Characteristics
Rigid Inflatable Hulls [planing] SPR p.6
  Rigid vee-bottom
  High stability
  High load capacity
  Exceptional seaworthiness in rough water

## Slide 7: Hull Types and Characteristics
Multi-Hulls [planing] SPR p.6
  Resist rolling
  Good steering ability at speed
  Large turning radius
  Shallow draft

## Slide 8: Hull Types and Characteristics
Round Bottom [displacement] SPR p.4
  Glide through water efficiently
  Speed is limited by length (hull speed)
  Usually have keel or chine for stability
  Good load bearing capability

## Slide 9: Parts of the Boat SPR p.11

## Slide 10: Propellers SPH SPR p.8
How propellers work
  Thrust
  Rotation [right-screw most popular]
    Side force (prop walk)
      More noticeable in reverse – esp. on fixed propeller
  Diameter
  Pitch
    Distance propeller would move in one revolution if turning in solid material
      ie 17” pitch propeller would move 17” inches
  Propeller size = diameter + pitch
    Smaller diameter + higher pitch used on high-speed boats
    Larger diameter + lower pitch used on slow-speed boats
  Stainless steel vs. Aluminum
  Linkage p.16

## Slide 11: Maneuvering Concepts
Uncontrollable forces affecting a boat
  Wind p.44
    Windage causes bow to fall off and boat to drift sideways
    Increased freeboard = increase windage effect
    Windage affects your turning arc
  Current
    Will move boat along as if on a conveyor belt
    Size, shape, etc. do not matter – current effects all things equally
    Yay for Lake Michigan! (mostly)

## Slide 12: Maneuvering Concepts
How boats turn
  Directed Thrust p.41
    Outboards, stern drives and jet drives
    When a propeller is turned at an angle, its thrust is directed at an angle, which turns the boat
    If propeller is not rotating then no thrust, so no steerage
  Rudder p.41
    Boats with a fixed propeller use a rudder to direct the flow of water
    Water flowing over the rudder creates lift (sideways force) and turns the boat
    No water flowing over the rudder = no steerage
  Pivot Point p.44
    In forward, a boats pivot point is located 25% to 40% aft from the bow
    Always steer the pivot point along the path you want to steer!
    Where is the pivot point on a boat in reverse?

## Slide 13: Maneuvering Concepts
Planning hulls behave like displacement hulls at low speed
At a certain speed, the hull goes through a transition stage called semi-displacement as it climbs the face of its bow wave p.47
Once the boat moves over the top of its bow wave, it levels off and begins to plane
  Where is the most optimum fuel consumption for a planing hull?
    Just as the boat has come comfortably on a plane

## Slide 14: Safety Equipment SPR p.83
PFDs
  Five types of PFDs
    Type I – Offshore Life jacket
      22 lbs of buoyancy for adults / 11 lbs for children
      Will turn unconscious person face-up
    Type II – Near-Shore Life Vest
      Min. of 15.5 lbs for adults / 11 lbs for children
      Will turn some unconscious people face-up
    Type III – Flotation Aid
      Buoyancy the same as Type II
      Will not turn unconscious person face-up
      Most common
    Type IV – Throwable Device
    Type V – Special use Devices
      Inflatable vests, etc.
      No inherent buoyancy
      Must be worn!

## Slide 15: Safety Equipment
PFDs
  Proper use of PFDs is integral!
    Should fit snugly but still allow movement
    If you can pull it up around your head on land, the same thing will happen in the water
    Any PFD with a tear or hole in it is no longer Coast Guard approved

## Slide 16: Safety Equipment
Federal Requirements for boats under 26ft
  One life jacket for each person on board. Must be readily available.
    Children under 13 MUST wear a lifejacket while underway (on any size vessel) unless below decks or in an enclosed cabin
  Over 16ft – one Type IV throwable device
  Sound producing device p.85
    Air horn, whistle, manual horn, etc.
  Fire extinguisher p.85
    Under 26ft – one B-I
      A – combustible material (wood)
      B – flammable liquids (gas)
      C – electrical (wiring)
      D – combustible metals (magnesium)
  Under 16ft - Visual distress signals if used at night p.84
  16ft up – MUST carry approved day/night visual distress signals

## Slide 17: Safety Equipment
Recommended Requirements
  Anchor + rode
  VHF Radio
  Knife
  First Aid Kit
  Spare parts / tool kit
  Oars
  Hand bilge pump
  Tow line / spare line

## Slide 18: Safety Equipment
Rescue Gear
  Boat hook
  Throw line
  Bridle for towing + tow line
  Spare boat parts
    Line, shackles, pins, blocks, sail tape, etc.

## Slide 19: Registration Information p.82
Hull Identification Number
Registration numbers and form
  Boat must be registered in its state of principal use or federally documented
  ‘IL’ numbers must be displayed on each side of the bow in letters at least 3” high
  Registration must be aboard vessel at all times
Max capacity plate
  Displays maximum weight and # of passengers (# of passengers takes precedence)
  Displays maximum horsepower engine (on outboard)
  Displays maximum weight capacity of all passengers, engine and gear
  Capacity equation: L x B / 15

## Slide 20: Some State Specific Info
Marine Heads: No marine head (toilet) on any watercraft used upon waters of this state may be so constructed and operated as to permit the discharge of any sewage into the waters directly or indirectly.
Battery Covers: Storage batteries shall be provided with suitable supports and secured against shifting. Batteries shall be equipped with nonconductive shielding means to prevent accidental shorting.
Unlawful Operation at Night: No person shall operate a personal watercraft or a specialty prop craft between the hours of sunset and sunrise.
Age of Operator:
1. No person under 10 years of age may operate a motor boat.
2. Persons at least 10 years of age and less than 12 years of age may operate a motorboat only if:
a. they are accompanied on the motorboat and under the direct control of a parent or guardian, or a person at least 18 years of age designated by a parent or guardian.
3. Persons at least 12 years of age and less than 18 years of age may operate a motorboat only if:
a. they are accompanied on the motorboat and under the direct
control of a parent or guardian or
b. a person at least 18 years of age designated by a parent or guardian or
c. such motorboat operator is in possession of a Boating Safety Certificate issued by the Department of Natural Resources, Division of Education or a valid certificate issued by another state, a province of the Dominion of Canada, the United States Coast Guard Auxiliary or the United States Power Squadron.

## Slide 21: Engine Information SPR p.13
Outboards
  Engine mounted on transom of boat
  2hp – 350+ hp
  2-stroke or 4-stroke
    2-strokes fire once every revolution of the crankshaft
        Power / intake-exhaust; compression
    4-strokes fire once every 2 revolutions of the crankshaft
        Intake – compression – power - exhaust
    2-strokes use a gas/oil mixture
    4-strokes use straight gas (oil is in the crankcase)
    Traditional 2-strokes are becoming obsolete
      Bad for the environment
      Less fuel efficient

## Slide 22: Engine Information
Outboards
  Variable shaft lengths
  Can be tilted all the way up or removed for storage

## Slide 23: Engine Information
Parts of an outboard engine SPR p.14

## Slide 24: Engine Information
Inboards SPR p.20 and p.41
  Engine mounted inside boat
  Gasoline or diesel
    Diesel is safer than gas – less risk for fire
    Gas inboards MUST have a backfire flame arrestor
  3 types of drive options:
    Fixed propeller drives
      Prop shaft passes through bottom of boat
      Steered by a rudder
    Stern drive (I/O)
      Engine mounted inside and the power train goes through transom to the stern drive
      Stern drive has tilt and trim similar to an outboard
    Jet drive
      Impeller accelerates water through a nozzle to produce propulsive thrust

## Slide 25: Engine Information
Proper fueling procedures SPR p.18 & 25
Common fueling mistakes
  Forget to vent the jerry can
  Nozzle not tightly attached to jerry can
  Overfilling
  Pouring one tank straight into another without a funnel or nozzle
  Pouring fuel into a deck fill that is NOT for fuel

## Slide 26: Engine Information
Proper start-up procedures for gas engines SPR p.16 & 21
  Inspect all hoses and wires
  Check fuel, oil and transmission fluid levels
  Run blower for 4 min (inboards)
  Lower engine into water (outboards and I/Os)
  Pump fuel primer bulb until firm, open vent
  Ensure that gear shift is in neutral
  Attach stop switch (kill switch)
  Pull cord / turn key to start
    Use choke and adjust idle as needed until running smoothly
  Once running, MAKE SURE THERE IS A STREAM OF WATER FLOWING FROM THE INSPECTION OUTLET
  Check gauges

## Slide 27: Engine Information
Gauge Guidelines
  Hour Meter
  Volt Meter –
    12+ volts
  Oil Pressure –
    MINIMUM of 20 PSI
  RPM –
    MAX Idle RPM of 800
  Temperature –
    140-160 is normal; 180+ is overheating

## Slide 28: Engine Information
Troubleshooting
  Fuel – Spark – Compression!
  Nothing happens when you turn the key
    Spark – is the battery dead? Are you in neutral?
  Engine turns over but won’t catch
    Fuel – is the engine getting gas? Is there water in the gas? Is the fuel line attached backwards?
    STOP SWITCH!
  Engine runs fine at idle but kills when at higher RPM
    Spark – bad spark plug? Loose spark plug lead?

## Slide 29: Pre-Boarding Preparation
Check weather conditions SPR p.29
  Not just for today but for yesterday and tomorrow!
  Internet
    Weather.com
    Sailflow.com
    Intellicast.com
    NOAA.gov
  VHF
    wx channels – broadcast continual marine forecasts

## Slide 30: Pre-Boarding Preparation
Understand local weather patterns
  Hot city + cool water = onshore breeze (only extends a few miles out)
  Cool city + warm water = offshore breeze
  Where direction does weather usually come from?
  What weather issues will most likely affect you?
      Northeastern = cold and wavy
      Northerly breeze on hot day = fog
      Southwestern = flat and puffy
          *what is fetch?
  What is a seiche?

## Slide 31: Pre-Boarding Preparation
Check tides and currents
  Not an huge issue on Lake Michigan
  Occasional current in mouths of harbors depending on wave/swell direction
      To check current, use a current stick or observe motion of water around a fixed object
      Belmont is particularly prone to current in the mouth of the harbor when there is an onshore breeze

## Slide 32: Pre-Boarding Preparation
File a float plan SPR p.31

## Slide 33: Pre-Boarding Preparation
Complete vessel checklist

## Slide 34: BREAK

## Slide 35: Boat Operation
Departing and returning to a dock
  Lynn’s rules of docking:
      Approach a dock as fast as you want to hit it.
      You will hit a dock eventually. Try to do it when no one else is around.
      Feel free to laugh at other’s docking mishaps after you have rendered assistance.
      Don’t forget – docking is a spectator sport!

## Slide 36: Boat Operation SPR p.54
Departing and returning to a dock (for real)
  Wind and current play MAJOR factors into docking. Always plan ahead to account for both.
  Try to dock on the leeward side if you are going to be staying for any length of time.
  Have lines and fenders ready BEFORE getting to the dock.
  Depending on the wind, you should be approaching from anywhere between 20-45 degrees.
  You should be able to bring boat to stop at dock without using lines to stop you.

## Slide 37: Boat Operation
Departing and returning to a dock
  Things to avoid:
    NEVER try to stop a boat without using a cleat
    NEVER put your body between a boat and a dock - bones are harder to repair than fiberglass!
    NEVER do the leap of faith onto the dock
    NEVER jump off the bow and pull it in as fast and tightly as you can

## Slide 38: Boat Operation
Departing and returning to a dock (video)

## Slide 39: Boat Operation
Departing and returning to a dock SPR p.38
  Proper line usage:

## Slide 40: Boat Operation
Proper boat storage – At the dock
  Engine raised and flushed (well….maybe)
  Steering wheel turned so steering arm is enclosed
  Lines checked and flemished
  Fenders hung at proper height
  Battery switched off (if appropriate)
  Any gear that was used stowed appropriately
  Bilge checked
  Garbage emptied

## Slide 41: Boat Maneuvering
Slow speed maneuvering
  Start, stop, reverse SPR p.40
  Minimum control speed SPR p.45 (video)
  Pivot turn SPR p.52 & p.59 (video)
  Holding position SPR p.46 (video)
    Downwind / upwind
  Approaching a mooring (video)

## Slide 42: Boat Maneuvering
Planing maneuvers
  Planing turns
    High speed slalom (avoidance turns) SPR p.51
  High speed stop (video) SPR p.53

## Slide 43: Boat Operation
To the boats!

## Slide 44: Boat Operation
Proper boat storage – Ashore
  Trailer guidelines p.143
    Be diligent with checking all aspects of trailer and connection
    Don’t settle – if boat isn’t seated properly, redo it
    Always remember to raise your engine before driving up the ramp!
    Check your tie downs multiple times.

## Slide 45: Knots
www.animatedknots.com
  Cleat hitch
  Bowline
  Round turn w/2 half hitches
  Sheet bend
  Coiling and heaving

## Slide 46: LUNCH

## Slide 47: Person in the Water
Proper Recovery Technique (SPR p.137)
  Yell ‘man overboard’!
  Driver immediately turns towards person swinging his propeller away from them
  Assign spotter
      MOST IMPORTANT PERSON
  Throw flotation devices towards PIW
  Circle around until able to approach from a DOWNWIND position
  Approach PIW on driver’s side and glide to a stop next to him/her [MUST BE IN NEUTRAL GEAR]
  Throw a looped rope and attach person to boat
  *****turn engine off*****
  Assist person into boat and care for

## Slide 48: Person in the Water
Proper Recovery Technique (video)